## Slide 1: An Overview of the Aircraft TC Measurement: From Present Capabilities to Future Needs
1Zorana Jelenak, 1Paul Chang, 2Ralph Foster,
3Heather Holbach, and 3Mark Bourassa
NOAA/NESDIS/STAR
2APL
3FSU

## Slide 2
Tail Doppler Radar
C-band
X-band
Ku-band
Ka-band
W-Band
antenna
Wind Lidar
Compact Ramen Lidar
Lidar
IWRAP
KaIA
Altius-600
Black Swift S0
Atmospheric Profiling
Radio Occultation
W-band

## Slide 3
Instrument | Aircraft | Measurements
GPS Dropsondes | C130, P3, G-IV | Atmospheric wind, temperature and humidity profiles
Stepped Frequency Microwave Radiometer | C130, P3, G-IV | C-band, nadir looking, Surface wind speed, rain rate
Imaging Wind and Rain Airborne Profiler (IWRAP) | P3 | Ocean Surface Vector Winds, (scatterometry) C, Ku, VV, HH, VH
Ka-band Interferometric Altimeter (KaIA) | P3 | Significant wave height, relative ocean height, & wind speed (lower speed regimes), precip profiles at Ka & Ku
Wide Swath Radar Altimeter (WSRA) | P3 | Significant wave height and directional wave spectra, wind speed (lower speed regimes), rain rate, Ku-band
Surface Wind Measurements
Aircraft Instrumentation
IWRAP
OSVW
Dropsonde+SFMR
KaIA
SWH
WSRA
SWH + Wave Spectra
Notes: Microphysics Spirals
Idalia - 20230829I1 - 1 spiral
Tammy - 20231019I1 - 1 spiral
Tammy - 20231021I1 - 1 spiral
Tammy - 20231022I1 - 2 spirals

## Slide 4: First Extreme Surface Wind Measurements
1997
Franklin at al 2003:
10m Surface Wind: WL150
1981/2005-present
Klotz (2014)
Sapp (2019)

## Slide 5
Comparison between SFMR and dropsonde WL wind computed from the WL150 algorithm using different layer height
Comparison between SFMR and dropsonde WL wind computed from the WL150 algorithm using different layer width
Bias and SD are significantly reduced when averaging the dropsonde readings over a layer thinner than the nominal 150-m layer. The dropsonde winds averaged over a 25-m-layer are more representative of the 10-m winds
Bias and SD increase when averaging the dropsonde readings over a layer at mean altitudes higher than the nominal 85 m. The WL150 scaling factor should be function of the mean layer height
Take away: The dropsonde WL150 winds can introduce noise and biases when converted into 10-m surface winds. The dropsonde surface winds estimated from the WL150 algorithm should be used with caution for cal/val [Polverari et al., IEEE TGRS, 2022]
On dropsonde surface-adjusted winds and their use for the SFMR wind speed calibration
Polverari at al 2022

## Slide 6: Holbach and Bourassa 2023 U10 vs WL150
This comparison is restricted to conditions when we can find a log profile, which are conditions that favor a good comparison to WL150 winds.
Variability increases as some function of wind speed
  Which is expected
Good agreement at lower speeds
  15 < u10 < 35 ms-1
WL150 is biased slightly high from ~35-50 ms-1 compared to our log-profile u10
WL150 significantly low biased above ~55 ms-1 compared to our log-profile u10

## Slide 7: ScatSat GMF – IWRAP Ku@50° Klotz 2014 RTM - SFMR

## Slide 8: ScatSat GMF – IWRAP Ku@50° Sapp 2019 RTM - SFMR

## Slide 9: NSCAT4 GMF –IWRAP Ku@50° Sapp 2019 RTM - SFMR

## Slide 10: Case of Hurricane Lee Sep 8th, 2023 NE Eyewall Winds: Cat 5 or 2-3?
SFMR surface wind measurements: Physical or Artificial?
  Flight path along storm motion – highest waves – wave impact on Tb’s?
  Storm just underwent RI was there extreme momentum transfer to the surface?
  GMF?
To answer cases like Lee we really need to know what was happening above the surface

## Slide 11: To understand Surface Winds Means We need to Understand What is happening within HBL
IWRAP-Imaging Wind and Rain Airborn Profiler (UMASS/NESDIS)
  Providing continuous real-time ocean surface winds and fine resolution real-time Doppler velocity and reflectivity profiles below the aircraft to just above the surface
  Connecting flight level, surface SFMR and sonde observations
  Providing new insite in physical processes of the HBL from very fine resolution measurements that will hopefully lead to better model parametarization
TDR
Reflectivity
SFMR

## Slide 12
Case of large wind overestimation

## Slide 13
Case of large wind overestimation

## Slide 14
Case of large wind overestimation

## Slide 15: Goal for datasets:
Consistent physics in remote sensing and boundary-layer modeling

## Slide 16: Look at TCBL Rolls with IWRAP and SAR Ralph Foster 2024
Upper: IWRAP
Lower: SAR-derived
Hurricane Larry (2021) Coincident IWRAP and SAR
Urad
Vtan
Significant Perturbation wind (r-z slice)
Upper: Upar: horizontal component of overturning flow (nearly radial)
Lower: Uperp: horizontal along-roll flow (in/out of page; nearly azimuthal)

## Slide 17: Look at TCBL Rolls with IWRAP and SAR Ralph Foster 2024
Upper: IWRAP filtered to
Lower: SAR-predicted (nonlinear) roll circulation
Note:
Roll circulations “lean into mean shear” (neutral stratification)
Uperp largest in lower PBL, “stretches-around” above
Similar phasing in theory and IWRAP
Structures are asymmetric  enhance fluxes

## Slide 18
Narrow spectral peaks indicate boundary-layer rolls in a similar manner to those detected by P3 aircraft in Hurricane Isidore (J. Zhang et al. 2008)
Saildrone
sUAS
Look at TCBL Rolls with sUAS and Saildrone J. Zhang 2024 preliminary results

## Slide 19
Sharp increase in stress when rolls emerge
Flux Buoy Data
No sharp increase in stress when rolls emerge
ERA5
Atlantic Trade Winds Region Upwind of Bermuda
Mass of data is here
Scattered outliers

## Slide 20: Wind Wave Growth in Hurricanes from KaIA and Measurements SFMR
15
10
5
5
10
15
0
10
10
20
20
30
30
40
40
Kaia Significant Wave Height [m]
SFMR Wind Speed [m/s]
Storm motion speed
Jelenak at al 2024 AMS

## Slide 21: Wind Wave Growth in Hurricanes from IFREMER WW3
15
10
5
5
10
15
0
10
10
20
20
30
30
40
40
Kaia Significant Wave Height [m]
WW3 Wind Speed [m/s]
Storm motion speed
Jelenak at al 2024 AMS
Model wave growth parameterization far from observations

## Slide 22
C130 P3 G4
Operational
Flight Level TDR MMR
ADWL
W-Radar
UAS
ARO
Microphysics Probes
Flight Level
TDR
Reflectivity
GPS Sonde + SFMR
MMR
X-Band Radar
IWRAP
KaIA WSRA
WSRA SWH
KaIA
Quasi-Operational
Research
Surface waves
OSVW
Rain Rate
3D Winds
3D Reflectivity
Surface winds
Rain Rate
3D Winds
3D Reflectivity
3D winds in clear sky

## Slide 23: Future
NOAA is moving away from the P-3 platform by 2030
We need recommendations from community regarding next generation aircraft instruments
  What measurements should be sustained
    No plans for replacement of any operational instruments
    TDR replacement plan is still uncertain
  What research measurements would be good to transition to operations
    There is transition plan for WSRA instrument
  What new measurements are needed?