## Slide 1
Status and recent developments of the EUMETSAT scatterometer missions
S Linow, N Khosravi, C Anderson, S Lupemba, M Cloarec
IOVWST Salt Lake City
29 May 2024

## Slide 2: Agenda
EPS-SG
Overview
SCA
Update on the mission status, planned activities
ASCAT
Instrument status and current work

## Slide 3: EPS-SG Objectives
  Primary mission: further improve observational inputs to Numerical Weather Prediction models.
  Continuation and enhancement of service from mid-morning polar orbit in 2025 – 2046 timeframe
  Significant contributions to other real time applications: Nowcasting at high latitudes; Marine meteorology and operational oceanography; Operational hydrology; Air quality monitoring.
  Climate monitoring: expand by 20+ years the climate data records initiated in 2006 with EPS (first generation).

## Slide 4: EPS-SG: Metop-SG satellites and instruments
SCA
RO
ICI
MWI
3MI
IASI-NG
MWS
Sentinel-5
MetImage
RO
Sat-A
Sat-B

## Slide 5: EUMETSAT scatterometer missions
03
04
05
06
07
08
09
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
31
32
33
34
35
36
37
38
39
40
YEAR...
EUMETSAT POLAR SYSTEM (EPS)
METOP-SG A: SOUNDING AND IMAGERY
METOP-SG B: MICROWAVE IMAGERY
EUMETSAT POLAR SYSTEM SECOND GENERATION (EPS-SG)
METOP-A
METOP-B
METOP-C
03
04
05
06
07
08
09
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
31
32
33
34
35
36
37
38
39
40
YEAR...
Metop
ASCAT-A (19 October 2006 – 15 November 2021)
ASCAT-B (launched 17 September 2012)
ASCAT-C (launched 07 November 2018)
Metop-SG
Scatterometer instruments (SCA) are on the SAT‐B series
SG-A1 launch planned for Q1/2025
SG-B1 launch planned for Q1/2026
[https://www.eumetsat.int/planned-launches]

## Slide 6: Scatterometer instruments
Second Generation – SCA
Frequency 5.355 GHz (C-band)
Swath width ~650 km
Incidence angles
  20° to 53.7° (mid beams)
  28.4° to 65° (side beams)
Polarizations: VV plus HH + HV + VH on mid-beams for improved high winds retrieval
First Generation – ASCAT
Frequency 5.255 GHz (C-band)
Swath width 550 km
Incidence angles
  25° to 53° (mid beams)
  34° to 65° (side beams)
Polarization: VV
© Airbus
ASCAT-C Level-1 backscatter triplets
Level-2 winds
© EUMETSAT / OSI SAF / KNMI
Storm Eunice
18. February 2022, RGB composite.

## Slide 7: EPS-SG SCA processing chain and products
EUMETSAT HQ
EUMETSAT SAF network:
OSI SAF + H SAF
EUMETSAT internal products
Level-0
  unprocessed data
Level-1A
  radiometric and spectral corrections and calibration factors
  telemetry
Level-1B full resolution (SZF)
  Radiometrically calibrated backscattering coefficients
  Geolocation in the original range location
  Quality flags
Level-1B resampled (SZR)
  Radiometrically calibrated backscattering coefficients
  Resampled on a swath grid
  Quality flags
Level-2
  Soil moisture
  Ocean surface wind vectors
Level-3
  Sea ice parameters (ice edge, type, low-resolution drift)

## Slide 8: L1 product dissemination
Timeliness
Global data: target 70 min
Regional data: target 30 min
Product ID | Global / Regional | EUMETCAST | Others | Destination (Others) | Archive
SCA-1B-SZF | G |  | NetCDF-4 | KNMI | BUFR NetCDF-4
SCA-1B-SZR | G | BUFR NetCDF-4 |  |  | BUFR NetCDF-4
SCA-1B-SZF | R |  | NetCDF-4 | KNMI | BUFR NetCDF-4
SCA-1B-SZR | R | BUFR NetCDF-4 |  |  | BUFR NetCDF-4
Some updates expected.
No dissemination via GTS is currently planned for SCA L1B data.

## Slide 9: SCA summary and outlook
SCA will ensure continuity of the EUMETSAT scatterometer missions for a period of >> 30 years
Currently preparing cal/val activities and supporting the development of the operational processing facilities
Finished final pre-launch versions of processing specs, test data set and cal/val plan
SCA cal/val will follow the well-established approach used for ASCAT:
  Validation using natural targets to assess long-term stability
  Ground-based transponders as absolute reference

## Slide 10: ASCAT status
Ongoing activities
Reprocessing the full ASCAT-A mission to provide a consistent time series of the full mission duration
Small evolution of the L1 processor – introduction of a new land-sea mask (fix known issues with the current one, is now consistent with the one for SCA)
Figure: raw noise powers, unitless
Upcoming
Will continue with ASCAT-B and ASCAT-C long-term behaviour assessment and reprocessing
Investigate noise/RFI evolution – this is highly problematic for land applications

## Slide 11: ASCAT-A long-term behaviour
Difference between the Gamma-0 obtained from descending and ascending orbits over the rainforest
Discrepancy between ascending and descending orbits, starting around 2019
Drift documented by Ricciardulli et al.* starts around the same time
Global ocean
Similar trend in the differences between the opposing beams
Also here, different spatial sampling of ASCAT-A and ASCAT-B
Amazon rainforest
* A Stable Satellite Wind Climate Data Record for Climate Variability Studies, Lucrezia Ricciardulli, Andrew Manaster, Thomas Meissner, and Carl Mears, Remote Sensing Systems, Santa Rosa, CA, USA, IOVWST 2023

## Slide 12: ASCAT-A long-term behaviour
ASCAT-A ground track
The last inclination maintenance of ASCAT-A occurred on 31.08.2016
after that, a slow drift has started leading to the local time of the ascending node to be shifted to about 90 minutes earlier by the end of the mission i.e., ~ 20:00 for ascending and ~08:00 for descending orbits.
ASCAT A and B fractional swath overlap for ascending passes (daily)
Drift observed since 2018 is most likely caused by different spatial sampling due to the drifting ground track of ASCAT-A, and is not a calibration issue

## Slide 13
Thank you!
Questions are welcome.