## Slide 1
IOVWST – May 29-31, 2024
NOAA’s Ultra High Resolution ASCAT Tropical Cyclone Wind Products
Seubson (Golf) Soisuvarn1,2, Suleiman Alsweiss1,3, Zorana Jelenak1,2, Paul S. Chang1, Qi Zhu1,3, Faozi Said1,3,
Joseph Sapp1,3 and Christopher Jackson1
1NOAA/NESDIS/STAR
2UCAR
3Global Science & Technology, Inc.
The views, opinions, and findings in this report are those of the authors and should not be construed as an official NOAA or U.S. government position or policy.

## Slide 2: Scatterometer Spatial Resolution Enhancement (BYU David Long)
25 km gridded (grd)
AVE (2.225 km pixels)

## Slide 3: Motivation – Scandies Rose sinking 2019
X
Scandies Rose sinking
The National Transportation Safety Board said the vessel’s inaccurate stability instructions combined with heavy lopsided ice accumulation due to wind and sea conditions, which were more extreme than forecasted during the voyage, caused the vessel to sink near Sutwik Island.
X
Notes: “Commercial fishing in 2019 was not just one of the most deadly occupations in America, it was the most deadly occupation in America,” said NTSB Chairman Robert Sumwalt during Tuesday morning’s video conference meeting. “Commercial fishing had a fatality rate of 145 fatalities per 100,000 full-time employees. Compare that to the average of all workers, which is 3.5 fatalities per 100,000.”

## Slide 4: 12.5km Standard ASCAT vs. UHR ASCAT
UHR outer swath extended for 75 km wider than the standard product swath
UHR wind reported every 1.5 km grid spacing
UHR winds up to 1 km of the coast vs 5-30 km for the 12.5 km product
UHR high wind retrievals rescaled utilizing SFMR measurements
UHR wind direction ambiguity removal initialized by utilizing the 12.5 km directions
  Reveals finer details in wind field but noisier than the original 12.5 km wind product

## Slide 6
34-knot radii remain unchanged

## Slide 8
UHR Processing Without Coastal Correction
Maximum Wind 50 m/s

## Slide 9
UHR Processing With Coastal Correction
Maximum Wind 41.1 m/s

## Slide 10
UHR Processing With Coastal Correction and High Wind GMF
Maximum Wind 53.6 m/s

## Slide 11: Validation: Model, Buoys, IWRAP, SFMR
S. Soisuvarn, Z. Jelenak, P. S. Chang, Q. Zhu and C. G. Shoup, "High-Resolution Coastal Winds From the NOAA Near Real-Time ASCAT Processor," in IEEE Transactions on Geoscience and Remote Sensing, vol. 61, pp. 1-12, 2023, Art no. 5208612, doi: 10.1109/TGRS.2023.3279764
NWP
Buoys
IWRAP
SFMR

## Slide 12: Coastal Winds Performance

## Slide 13: Center Fixes

## Slide 14: Storm Circulation and Center Determination
550 km
45
Left swath
550 km
Right swath
90
135

## Slide 15: Example: Hurricane Lee 09/09/2023 – cont.
_
=
The intersection of the two red lines is the storm center
Forward Look Sigma0
Aft Look
Sigma0

## Slide 16: Ophelia

## Slide 17: Belal

## Slide 18
x
x
x
x
x
No circulation
but more organized system
No circulation
Closed circulation
Distorted closed circulation
Still no closed circulation
Even more organized

## Slide 19: Max Wind Determination

## Slide 20: MAX Wind Determination
85%
90%
95%
99%
Determine radius on max winds in all 4 quadrants
Determine wind speed distribution within the largest radius
Determine winds within 85, 90, 95 and 99 percentile of the distribution
Check for consistencies
Check location within swath

## Slide 21
85%
90%
99%
Black pixels represent WVCs from which the mean max wind was calculated
95%

## Slide 22: Maximum Wind
Maximum wind was calculated as mean of the 85, 90, 95 and 99 percentile of winds within maximum of RMW within four quadrants
  Using 95% or higher yields cat 3 winds
  Using lower % results in cat 2 winds
Use in combination with other data to determine max
 | 85% [kts] | 90% [kts] | 95% [kts] | 99% [kts] # number of WVC
ASCAT-B 4:05Z | 88.2 | 90 | 95 | 98.89 #7
ASCAT-C 4:58Z | 86 | 90 | 94 | 99.25 #7
ASCAT-B 16:36Z | 81 | 83 | 85.6 | 88.25 #12
ASCAT-C 17:28Z | 86 | 90 | 94.4 | 98.75 #15

## Slide 23: Important to Remember: C-band is Attenuated in Rain

## Slide 24: Max Wind Determination (95%) vs Best Track
ASCAT UHR
ASCAT NOAA 12.5

## Slide 26: Edge Issues

## Slide 27: All winds above 30m/s with Mid Beam Incidence angle <25° should be omitted from Max Wind and Wind Radii Estimations
550 km
45
Left swath
550 km
Right swath
90
135

## Slide 28: Wind Radii Determination

## Slide 29: Analyzed Wind Radii @4:05z 08/18/2023
New UHR Products – In Testing/Validation Phase

## Slide 30
LEE case study
SAR time:2023/09/12-10:13 | ASCAT time:2023/09/12-14:34 (4hr+ time diff.)

## Slide 31
34kts
50kts
64kts

## Slide 32: ASCAT UHR Data Availability
Data available in NRT
https://manati.star.nesdis.noaa.gov/UHR_ASCAT/
Images
https://manati.star.nesdis.noaa.gov/datasets/ASCATCStorm.php

## Slide 33: UHR ASCAT Summary
  UHR winds reveal finer spatial structures and higher wind speeds
    UHR ASCAT = “coarse resolution SAR”
  High wind performance with respect to IWRAP Ku and C-band measurements valid up to 45 m/s
  Validation with SFMR shows a correlation of 0.9 and a 2.67 m/s low bias (We believe this is a SFMR problem not ASCAT)
  For closed circulation and storm center detection Fore-Aft Sigma0 imagery should be considered
    UHR wind direction too noisy
  UHR ASCAT maximum wind should be considered together with ASCAT 12.5km wind directions and rain flag
  Capable of retrieving 34, 50 and 64 knot wind radii

## Slide 34: Backup slides

## Slide 35
_
=
Forward Look Sigma0
Aft Look
Sigma0

## Slide 36: Saola

## Slide 37: Anggrek

## Slide 38: Tammy

## Slide 39: Belal

## Slide 40: Saola