## Slide 1: Retrieval of Ocean Surface Wind Speed for Future Passive Microwave Imager: MWI
IOVWST, 28-05-2024
Sisma Samuel, Anton Verhoef, Ad Stoffelen

## Slide 2: Outline
Passive Microwave Remote Sensing: Introduction
Microwave Imager onboard Metop-SG
1D-Var Retrieval of wind speed
Comparison of
        Simulated vs Observed Brightness Temperature
        Retrieved Wind speed vs model wind speed

## Slide 3: Passive Microwave Remote Sensing: Introduction
Observes the thermal emissions- Brightness temperature
22 GHz
183.3 GHz
©Ulaby et al. 2014
The longer wavelength of microwaves enables it to penetrate through clouds, haze, and dust
TSE- Surface emitted
TUP- Radiation upward by atmosphere
TSS- Surface scattered

## Slide 4: Microwave Imager
Microwave Imager (MWI) is a conically scanning Radiometer onboard Metop-SG
18 frequencies, 26 channels
Constant Zenith Angle ~ 53°
Swath 1700 km, 40 scans/min = 10 km/scan
No | Central frequency (GHz) | Bandwidth (MHz) | Polarisations | IFOV
1 | 18.7 | 200 | V, H | 50 km
2 | 23.8 | 400 | V, H | 50 km
3 | 31.4 | 200 | V, H | 30 km
4 | 50.3 | 180 | V, H | 30 km
5 | 52.8 | 400 | V, H | 30 km
6 | 53.24 | 400 | V, H | 30 km
7 | 53.75 | 400 | V, H | 30 km
8 | 89.0 | 400 | V, H | 10 km
9 | 118.7503±3.2 | 1000 | V | 10 km
10 | 118.7503±2.1 | 800 | V | 10 km
11 | 118.7503±1.4 | 800 | V | 10 km
12 | 118.7503±1.2 | 800 | V | 10 km
13 | 165.5±0.725 | 2700 | V | 10 km
14 | 183.31±7.0 | 4000 | V | 10 km
15 | 183.31±6.1 | 3000 | V | 10 km
16 | 183.31±4.9 | 3000 | V | 10 km
17 | 183.31±3.4 | 3000 | V | 10 km
18 | 183.31±2.0 | 3000 | V | 10 km

## Slide 5: Microwave Imager
Microwave Imager (MWI) is a conically scanning Radiometer onboard Metop-SG
18 frequencies, 26 channels
Constant Zenith Angle ~ 53°
Swath 1700 km, 40 scans/min = 10 km/scan
Channel No | Central frequency (GHz) | Bandwidth (MHz) | Polarisation | IFOV
12 | 19.35 | 355 | H | 25
13 | 19.35 | 365 | V | 25
14 | 22.235 | 407 | V | 25
15 | 37 | 1615 | H | 25
16 | 37 | 1545 | V | 25
Currently we make use of Special Sensor Microwave Imager/Sounder (SSMIS) for wind retrieval

## Slide 6: 1D-Var Retrieval of wind speed
1D-Var requires a background profile to derive first guess of atmospheric state- NWPSAF & ERA5 profiles
Input profile
Select matching profiles
Compute Brightness Temperature
Run 1D-Var
1D-Var
Converged
?
No
Matching profile is selected based on SST and windspeed
RTTOV calculates TB for each wavelength.
SURFEM model: for ocean surface emissivity
If yes, written to output.
Estimate optimal solution by minimizing cost function
TB filtering to avoid larger mismatch

## Slide 7: Simulated vs Observed Brightness Temperature-All sky Condition
19H
19V
37H
37V
22V
RTTOV calculates the TB for each channel based on the background atmospheric profiles
NWPSAF Profile

## Slide 8: Simulated vs Observed Brightness Temperature-All sky Condition
19H
19V
22V
37H
37V
RTTOV calculates the TB for each channel based on the background atmospheric profiles
ERA5 Profile

## Slide 9: Comparison of retrieved Wind speed to model windspeed
Radiometer wind speed (m/s)
Radiometer wind speed (m/s)
NWPSAF Profile
ERA5 Profile
Wind speed was estimated by minimizing the cost function

## Slide 10
Comparison of retrieved Wind speed: After Bias correction
Radiometer wind speed (m/s)
Radiometer wind speed (m/s)
NWPSAF Profile
ERA5 Profile
Average bias and Std Dev reduces after bias correction

## Slide 11: Attenuation effect of rain
Rain Flag:
TB (37V)-TB(37H)<50K
TB (19H)>165K
Goodberlet et al., 1989
Connor and Chang, 2000

## Slide 12: Simulated vs Observed Brightness Temperature: Rain Flag
19H
19V
22V
37H
37V
RTTOV calculates the TB for each channel based on the background atmospheric profiles.
~18% of points are removed after applying rain flag
NWPSAF Profile

## Slide 13: Simulated vs Observed Brightness Temperature: Rain Flag
19H
19V
22V
37H
37V
RTTOV calculates the TB for each channel based on the background atmospheric profiles.
~20% of points are removed after applying rain flag
ERA5 Profile

## Slide 14
Comparison of retrieved Wind speed: After bias correction
NWPSAF
ERA5
Radiometer wind speed (m/s)
Radiometer wind speed (m/s)
NWPSAF Profile
ERA5 Profile
Average bias and Std Dev reduces after bias correction for rain flag cases

## Slide 15: Conclusion
All-sky condition |  |  |  | Rain Flag | 
Before Bias Correction |  | After Bias Correction |  | After Bias Correction | 
Bias | Std Dev | Bias | Std Dev | Bias | Std Dev
0.49 | 0.84 | 0.21 | 0.82 | 0.18 | 0.80
0.88 | 1.18 | 0.62 | 1.16 | 0.63 | 1.10
Currently, we make use of the SSMIS onboard DMSP to prepare for future MWI retrievals.
The NWP SAF 1-Dimensional Variational Technique and Radiative transfer model (RTTOV) is used for the retrieval of near surface wind speed.
ERA5
NWPSAF
Thank you